## Slide 1: COLD WEATHER
Construction of Twins Baseball Stadium – Minneapolis, MN

## Slide 2: Cold Weather: Definition
Varies by region of the country
“Cold” temperatures < 40o F
“Cool” temperatures (40 - 60o F)
Temperature information inferred from www.cdc.gov
Taken from www.go-explore-trans.org

## Slide 3: Common Cold Weather Elements
Rain, freezing rain, snow, sleet, ice, and frost
  Damp or wet clothing makes the body feel colder
Wind
  “wind chill” causes the air to feel colder than it really is
Taken from www.cbc.ca

## Slide 4: Wind Chill Effect
For Example:
A temperature of 30 degrees Fahrenheit with a 40 mile per hour wind would feel like 13 degrees Fahrenheit.
mph | temp | 20 | 25 | 30 | 35 | 40
60 |  | -4 | 3 | 10 | 17 | 25
55 |  | -3 | 4 | 11 | 18 | 25
50 |  | -3 | 4 | 12 | 19 | 26
45 |  | -2 | 5 | 12 | 19 | 26
40 |  | -1 | 6 | 13 | 20 | 27
35 |  | 0 | 7 | 14 | 21 | 28
30 |  | 1 | 8 | 15 | 22 | 28
25 |  | 3 | 9 | 16 | 23 | 29
20 |  | 4 | 11 | 17 | 24 | 30
15 |  | 6 | 13 | 19 | 25 | 32
10 |  | 9 | 15 | 21 | 27 | 34
5 |  | 13 | 19 | 25 | 31 | 36

## Slide 5: Hazards
Loss of Grip Strength
  A study by Horvath and Freedman found that “grip strength decreased by one-fourth even though the cold exposure was of relatively short duration”.
  Could lead to dropping of equipment such has hammers or torches
  Horvath, S.M., and Freedman, A. The Influence of Cold upon the Efficiency of Man. Journal of Aviation Medicine, 18, 158-164, 1947.
Taken from journalistopia.com

## Slide 6: Hazards
Hypothermia
  Lowered core body temperature
  Drop in blood pressure
  Mental confusion
  Death (if left untreated)
Core Temp (°F) | Body’s Response
99.6 | Normal body temperature
96.8 | Metabolic rate increases
95 | Pronounced shivering
91.4 | Severe hypothermia
86 | Consciousness loss begins
75.2 | Pulmonary edema
68 | Cardiac Standstill

## Slide 7: Hazards
Frost
  Frost on roofs, scaffolding, ladders, etc, may present a danger of slipping and falling
  Leading cause of deaths in the construction industry due to cold weather
Frostbite
  Occurs when the body constricts blood flow to extremities in order to preserve core body temperature
  Prolonged exposure will lead to permanent cell damage

## Slide 8: Hazards
Unpredictable Conditions
  Cold weather changes many of the conditions on the construction site such as soil
    Equipment may become frozen to the ground
    Trench conditions may become unpredictable
    Excavated soil can freeze, becoming dangerous if loose
Taken from flickr.com/photos/ alohadave/2194113460/

## Slide 9: Fatalities
28 deaths attributed to cold weather conditions were investigated by OSHA from 1990 thru 2009
  Most death cases are attributed to slips and falls due to frost, ice, and snow
  Frozen soil conditions are also causal factors
  Source: Extracted from OSHA Accident Investigation Data 1990-2009

## Slide 10: Fatality Example
  A worker was staging bundles of shingles on the second story roof of a newly-constructed house. The worker was on the east side of the house near a valley when he slipped on frost or ice on the roof and fell 21 feet to the ground. He was transported to the hospital where he died the next day.
  Source: Extracted from OSHA Accident Investigation Data 1990-2009

## Slide 11: OSHA Regulations
1926.451(a)(17) addresses snow buildup
In a sample safety plan, OSHA regulations state:
  “When wet weather (rain, snow, or sleet) are present, roof sheathing operations shall be suspended unless safe footing can be assured for those workers installing sheathing”
Source: OSHA Regulations 1926

## Slide 12: Best Practices
PPE
  Care must be taken to properly cover all exposed skin with appropriate clothing made for the cold weather environment
  Cold Weather clothing should:
    Provide high insulation
    Allow Moisture to escape
    Waterproof
    Shed snow
    Allow air flow
    Not restrict movement
    Have minimum weight and bulk

## Slide 13: Best Practices
Provide an on-site break area that is heated and dry
  Require warm-up breaks based on
  length of shift and experienced
  temperature
Reduced visibility
  Use brightly colored signs
  Double check for workers in area
  Cease current construction work
  if visibility is significantly
  hampered by weather

## Slide 14: Best Practices
Environmental Awareness
  Checks should be made each morning for potential hazards that may have formed due to freezing overnight temperatures
  Strictly enforce pre-task planning and its documentation
Training
  Train workers in avoiding consequences of cold weather exposure
  Train workers in recognizing symptoms of hypothermia, frostbite, cold stress, and other cold-related illnesses.

## Slide 15: Best Practices
Use the buddy system so workers are never working alone in isolated areas
Food and Drink
  Be sure employees are staying well-hydrated
  Avoid caffeine, alcohol, and other drugs
  Consume high-calorie foods and sports drinks

## Slide 16
Think Safety
Work Safely