## Slide 1: Dump Trucks
Standard Safety Practices and Concerns

## Slide 2: Introduction:
Dump Trucks are a common piece of equipment utilized on virtually all construction sites.
Primary use: to haul loads of loose material such as soil, gravel, or dirt to and from jobsites.
Images source: Google Images

## Slide 3: Introduction:
Two Basic Kinds:
  Off road
  On road
Off- Road
On- Road

## Slide 4: Introduction:
Dump trucks are generally equipped with a hydraulically operated open-box bed hinged at the rear.
The front of the bed is lifted up to allow its contents to be deposited on the ground behind the truck at the site of delivery.
Cab
Bed
Hydraulic
Lift
Source: www.wikipedia.com

## Slide 5: Variety of Types:
  super dump trucks
Source: www.wikipedia.com
standard dump trucks
articulated dump trucks
  transfer dump trucks
  semi-trailer end and bottom
  dump trucks
double and triple trailer bottom dump trucks

## Slide 6: Primary Modes of Accident Causation:
  People being run over by dump trucks
Source: Jimmie Wayne Hinze

## Slide 7: Primary Modes of Accident Causation:
  People being run over by dump trucks:
    Example:
    “A laborer, was preparing the surface of a newly back-filled trench for placement of a black top patch in a roadway. The driver of a dump truck was attempting to back up to receive a load of dirt. The laborer was run over and killed. The vehicle's back-up alarm was found to be defective; it only worked intermittently.”
Source: 1999-2007 OSHA Fatality Data

## Slide 8: Primary Modes of Accident Causation:
  Trucks tip over due to uneven ground or poor distribution of load.
Source: http://www.construction-site-accident.com/lawyer/dump_truck_accidents.html

## Slide 9: Primary Modes of Accident Causation:
  Trucks tip over due to uneven ground or poor distribution of load.
    Example:
    An employee was using a dump truck to haul excavated material to a dump site on the next level up a mountain. It appeared that the operator backed his vehicle into place, dumped his load, and was lowering his bed when the soft surface of previously dumped material gave way. His wheels sank, causing his truck to roll backward down the slope. The truck struck range boulders that had been dumped near the bottom of the slope, rolled over three or four times, and continued. The employee was thrown out of the cab was killed.
Source: 1999-2007 OSHA Fatality Data

## Slide 10: Primary Modes of Accident Causation:
  Electrocution caused by the bed becoming attached to overhead power lines.
Image Source: http://www.elcosh.org

## Slide 11: Primary Modes of Accident Causation:
  Electrocution caused by the bed becoming attached to overhead power lines.
    Example:
    “An employee was dumping a load of stone at a temporary levee. The levee was being constructed to stem the flow of flood waters. He backed his dump truck into position and raised the semi-dump trailer to dump the load. The trailer contacted a 12.5-kilovolt overhead power line, which caused the truck tires to ignite. The employee jumped from his truck, but was electrocuted when he touched the truck while he was on the wet stone roadway.”
Source: 1999-2007 OSHA Fatality Data

## Slide 12: Primary Modes of Accident Causation:
  Being crushed or pinned by the collapsed bed due to pin or support malfunctioning.
Image Source: http://www.elcosh.org

## Slide 13: Primary Modes of Accident Causation:
    Being crushed or pinned by the collapsed bed due to pin or support malfunctioning.
    Example:
    “An employee was working on the hydraulic lift system of dump truck. He was adding a pump to increase the lifting capacity of the dump box. The dump box was elevated into position. While in the up position, the box was not blocked or cribbed as to prevent an accidental fall. Consequently, the dump box fell on the employee, crushing his head and neck. The injury resulted in a death.”
Source: 1999-2007 OSHA Fatality Data

## Slide 14: Dump Truck Dangers:
Source: http://images.google.com/imgres?imgurl=http://safetybootsandcrochet.files.wordpress.com

## Slide 15: Dump Truck Dangers:
Causes for tipping:
Stability is adversely affected by one or more of the following factors:
  the unit is not on a level surface when dumping
  a large amount of material is in the upper portion of the raised box
  material does not flow out of the top portion of the box, or does not flow out of one side of the top portion
  the rear wheels settle unevenly as the load moves to the rear during dumping
  wind may exert lateral loads, especially if the box is long, as is the case with end-dump semi-trailers.
Source: http://www.construction-site-accident.com/lawyer/dump_truck_accidents.html

## Slide 16: Dump Truck Dangers:
Causes for tipping:
Stability may also be affected by the unit's mechanical condition:
  poor rear suspension systems on one side of the vehicle
  uneven tire pressures in rear wheels
  worn or inadequate components of the lifting system such as pins
  worn or inadequate lifting cylinders.
Source: http://www.construction-site-accident.com/lawyer/dump_truck_accidents.html

## Slide 17: Breakdown of 388 Fatalities Involving Dump Trucks
Chart: 
| Struck by | Roll Over | Electrocution | Load Dumped on Victim | Crushed by Tailgate or Bed | Drowned
Column1 | 262 | 41 | 20 | 6 | 50 | 9

## Slide 18: Nature of Dump Truck Movement
Chart: 
| Forward | Reverse | Stationery
Column1 | 64 | 194 | 91
Note: Of 25 backup alarms that were not functioning on the dump trucks (all associated with fatalities), 23 resulted in deaths when traveling in reverse.

## Slide 19: Description of Victim
Chart: 
| Dump Truck Driver | Worker on the Ground | Driver of other Equipment | Worker Riding in/or the Dump Truck
Column1 | 76 | 218 | 16 | 8

## Slide 20: Task of Dump Truck
Chart: 
| Hauling Full Load | Traveling Empty | Being Loaded | Dumping | Standing Still | Being Repaired
Column1 | 80 | 16 | 12 | 60 | 11 | 38

## Slide 21: OSHA Regulations:
  1926.601 Motor Vehicles (b)
  All vehicles must have working:
  service brakes
  emergency brake system
  parking brake system.
  All vehicles need at least 2 head lights and 2 tail lights. Must have break lights.
Source: OSHA Standards 2005 subpart J-0

## Slide 22: OSHA Regulations:
1926.601 Motor Vehicles (b)
All vehicles must be equipped with operable audible warning device at the operator’s station.
If vehicle has no rear view than it needs a spotter or an audible signal when backing up.
OR
Source: OSHA Standards 2005 subpart J-0
BEEP…BEEP
WATCH OUT!

## Slide 23: OSHA Regulations:
1926.601 Motor Vehicles (b)
All vehicles with cabs must have a windshield & wipers.
    Broken glass must be replaced.
Defogging and defrosting devices are also required to ensure adequate visibility.
Req. Windshield wipers
Source: OSHA Standards 2005 subpart J-0

## Slide 24: OSHA Regulations:
1926.601 Motor Vehicles (b)
(6) All trucks must be equipped with a cab shield to prevent loose falling material from hitting the operator.
(7) Tools & Materials must be secured when being transported in the same compartment as workers.
(8) Vehicles used to transport employees must have a secured seat for each employee carried.
(9) All vehicles must be equipped with proper seatbelts.
Source: OSHA Standards 2005 subpart J-0

## Slide 25: OSHA Regulations:
1926.601 Motor Vehicle (b)
(10) Truck with dumping bodies must have locked support required when being repaired or maintained
(11) Levers that control the hoisting or dumping devices must have latch that prevents bumping controls & accidentally dumping or hoisting.
(12) Trip handles must be located so that the operator is not in the path of the dumping material.
Pins are attached to trucks to lock dump bodies in place to prevent accidental lowering.
Source: OSHA Standards 2005 subpart J-0
Locked support
activated inside cab

## Slide 26: OSHA Regulations:
OSHA requires trucks be checked at the beginning of each shift to be sure all parts are in operable condition.
  Defects found must be reported and the truck must be left out of services until repaired.
Steering mechanism
Engine
Tires
Operating controls
Seat belts

## Slide 27: Safety Precautions:
Operator’s guidelines:
  Dump trucks should only be operated by trained professionals.
  Operators must be well rested and attentive when operating this equipment.
  Operators must wear the required personal protective equipment
    This includes shoes , a seat belt and a hard hat when necessary.
  Operators should not use cell phones while operating this equipment

## Slide 28: Safety Precautions:
Equipment precautions:
  Trucks must be maintained in good working condition at all times.
  Before starting the truck, perform a pre-start check assess the surrounding environment.
  Communicate with surrounding workers to identify possible hazards or obstructions.

## Slide 29: Safety Precautions:
Maintenance:
  Check tire pressures daily. Tire pressures should be equal on each side of the vehicle.
  Examine and lubricate pins and bushings regularly.
  Inspect suspension systems under load to ensure that they work properly and provide even suspension. Weak suspension systems should be replaced immediately.
  Inspect hoist cylinders regularly. Worn cylinders should not be replaced with smaller cylinders or with cylinders rated at lower operating pressure.
  Make sure that repairs to boxes leave bottom and sides clear and unrestricted. Rough patchwork repairs near the top of the box can catch and hold sticky materials.
Source: http://www.construction-site-accident.com/lawyer/dump_truck_accidents.html

## Slide 30: Safety Precautions:
Loading:
Loading of the box front-to-back must meet allowable gross weight and axle weight limitations set by the Ministry of Transportation.
From side to side it is best to load as evenly as possible.
If material is likely to flow poorly, lighten up the load in the top end of the box. A slightly smaller load will be better than a full load that causes a tip-over.
Box liners will help most materials flow better during dumping. Liners also help to keep the box in good condition.
Source: http://www.construction-site-accident.com/lawyer/dump_truck_accidents.html

## Slide 31: Safety Precautions:
Check the Load:
  To avoid truck damage, the safety of others, and being cited.

## Slide 32: Safety Precautions:
Dumping:
Operators should be trained to recognize areas hazardous to dumping.
Before dumping, operators should ensure that the tailgate is unlocked and that the vehicle is on a reasonably level surface.
Before spreading material by dumping it from a moving truck, make sure that the entire length of travel is reasonably level.
Trucks should not dump when they are parked side by side with another vehicle.
Other personnel such as dozer operators, surveyors, and spotters should be warned not to work near a dumping truck in case it tips over.
Workers on foot should not congregate in areas where dumping is under way.
Source: http://www.construction-site-accident.com/lawyer/dump_truck_accidents.html

## Slide 33: Safety Precautions:
Always make sure tailgate is unlocked before raising body.
Be aware of the size of truck to avoid overhead power lines/overpasses when dumping.
Dump beds shall be fully lowered or blocked when being repaired or when not in use.

## Slide 34: Safety Precautions:
Tipping:
  Work on flat ground when possible.
  Choose the most appropriate travel route to avoid uneven surfaces and possible tipping.
  Do not hurry or take shortcuts.
  Advise when haul roads/ routes need maintenance.
Image Source: Google Images

## Slide 35
Think Safety
Work Safely